## Slide 1: Network Load Balancing with In-network Reordering Support for RDMA
Cha Hwan Song Xin Zhe Khooi Raj Joshi Inho Choi Jialin Li Mun Choon Chan

## Slide 2: Remote Direct Memory Access (RDMA)
RDMA is the emerging standard in modern DCs
RDMA + RPC
RDMA + Storage
RDMA + AI/ML
Versatility
Performance
High throughput
Low latency
Low CPU overhead
Application
Buffer
Host OS (TCP)
RDMA NIC
Production-level deployment in DCs
Practicality
[1] Gao, Yixiao, et al. “When cloud storage meets RDMA”. NSDI 2021 [2] Bai, Wei, et al. “Empowering azure storage with RDMA”. NSDI 2023
+ probably more !

## Slide 3: This Talk: Network Load Balancing for RDMA
Despite such benefits, RDMA does not fully exploit the high path diversity in DCNs.
Existing LB schemes do not fit well with RDMA.
Why, and what is the solution?

## Slide 4: Prior Load Balancing Designs
Per-flowlet
Per-flow
Per-packet
Fine-grained
Coarsed-grained
Reroute granularity

## Slide 5: Prior Load Balancing Designs
Per-flow [e.g., ECMP]
ECMP (Equal Cost Multi Path) is de-facto standard for RoCEv2*
* InfiniBand Trade Association. 2020. InfiniBand Architecture Specification Release 1.4 Annex A17: RoCEv2
H(Pkt) % 2 == 0
H(Pkt) % 2 == 1
e.g., Hashing 5-tuple to decide the
egress link
Cannot evenly distribute flows based on their sizes
RDMA over Converged Ethernet

## Slide 6: Prior Load Balancing Designs
Per-packet rerouting provides a near-optimal load balance
Per-packet [e.g., spraying, DRILL]
Rerouting decision for every packet
Spray, or to the smallest Eg.Queue
RDMA is highly sensitive to out-of-order packets
2
1
Out-of-order!
Resilient datacenter load balancing in the wild [SIGCOMM’17]

## Slide 7: Prior Load Balancing Designs
Out-of-order!
Per-packet rerouting provides a near-optimal load balance
Per-packet [e.g., spraying, DRILL]
Rerouting decision for every packet
Spray, or to the smallest Eg.Queue
RDMA is highly sensitive to out-of-order packets
Sender NVIDIA CX-6
Receiver NVIDIA CX-6
Tofino Switch
Randomly craft 1 out-of-order pkt
Unlike TCP, a “single” out-of-order packet largely increases FCT with spurious ReTx and rate decrease
FCT normalized to in-order msg | 10KB msg | 1MB msg
50th-percentile | 1.65x | 2.65x
99th-percentile | 1.25x | 3.27x

## Slide 8: Prior Load Balancing Designs
Per-flowlet rerouting avoids out-of-order arrivals via timegaps
Flowlet 1
Flowlet 2
Flowlet 3
Reroute only if there is enough inactive timegap between two packets
>∆
>∆
Per-flowlet [e.g., Conga, Letflow, PLB]
Hard to find time gaps in RDMA
CONGA: Distributed congestion-aware load balancing for datacenters [SIGCOMM’14]
Let it flow: Resilient asymmetric load balancing with flowlet switching [NSDI’17]
PLB: congestion signals are simple and effective for network load balancing [SIGCOMM’22]

## Slide 9: Prior Load Balancing Designs
Per-flowlet rerouting avoids out-of-order arrivals via timegaps
Per-flowlet [e.g., Conga, Letflow, PLB]
Flowlet 1
Flowlet 2
Flowlet 3
Reroute only if there is enough inactive timegap between two packets
>∆
>∆
Hard to find time gaps in RDMA
Experiment: A bulk data transfer with 8 concurrent connections
flowlet’s timegap threshold (∆)

## Slide 10: Prior Load Balancing Designs
Experiment: A bulk data transfer with 8 concurrent connections
Per-flowlet rerouting avoids out-of-order arrivals via timegaps
Per-flowlet [e.g., Conga, Letflow, PLB]
* Yuanwei Lu, et al., Multi-Path Transport for RDMA in Datacenters, [NSDI’18]
Less chances to reroute
HW-based packet pacing*
Batch process

## Slide 11: Design Goal
Preserving pkt order
Reroute granularity
Fine grained
How to get here?
In-order
Out-of-order
Coarsed grained
Better
Per-packet
Per-flow
Per-flowlet (for TCP)
Per-flowlet (for RDMA)

## Slide 12: Idea – In-network Packet Reordering
“Restore” packets back in-order before reaching to end-hosts

## Slide 13: Idea – In-network Packet Reordering
“Restore” packets back in-order before reaching to end-hosts
RDMA’s host OS bypass
Fixed-function RDMA HW
RDMA
End-host is not a viable option

## Slide 14: Idea – In-network Packet Reordering
“Restore” packets back in-order before reaching to end-hosts
Queue pause/ resume capability
Intel Tofino2 Programmable Switch
~128 FIFO queues per Eg. port
Opportunity

## Slide 15: Challenges in Packet Reordering on Switches
Hard to restore “arbitrary” packet orders on switches:
4
3
2
1
Next SEQ = 1
Costly to store pkts to FIFO queues and flush them
flush in relays
FIFO queues
  Lack of sorting primitives on switching hardware
Limited resource and time for storing and flushing packets at line-rate

## Slide 16: Challenges in Packet Reordering on Switches
Hard to restore “arbitrary” packet orders on switches:
4
3
2
1
Next SEQ = 1
Costly to store pkts to FIFO queues and flush them
flush in relays
FIFO queues
  Lack of sorting primitives on switching hardware
Limited resource and time for storing and flushing packets at line-rate
How to “constrain” the packet reordering patterns?

## Slide 17: ConWeave (short for Congestion Weaving)
High-level Overview
network
ConWeave SrcToR
ConWeave DstToR
Rerouting
Reordering
ToR-to-ToR mechanism, i.e., end-host agnostic

## Slide 18: ConWeave (short for Congestion Weaving)
High-level Overview
network
ConWeave SrcToR
ConWeave DstToR
Rerouting
Reordering
Hard to find time gaps
Arbitrary packet order is not manageable
Cautiously split and reroute flows for the ease of reordering

## Slide 19: ConWeave (short for Congestion Weaving)
Key Components in ConWeave
Path Monitoring
Agile and lightweight congestion detection
Path Selecting
Telemetry-driven congestion evasion
This Talk!
Cautious Rerouting
Tight incorporation with switch’s reordering capability
Pkt Reordering
Efficient queue flush via strict priority
* More details in the paper

## Slide 20: Cautious Rerouting
Reroute “only if” there is no inflight out-of-order packets
 Enable switch to reorder a flow using a single reorder queue
ConWeave SrcToR
ConWeave DstToR
Key Idea
Normal queue (for all flows)
Current path is congested!

## Slide 21: Cautious Rerouting
ConWeave SrcToR
ConWeave DstToR
T
Tag “TAIL” – last pkt before rerouting
Normal queue (for all flows)
Reroute “only if” there is no inflight out-of-order packets
 Enable switch to reorder a flow using a single reorder queue
Key Idea

## Slide 22: Cautious Rerouting
ConWeave SrcToR
ConWeave DstToR
T
Reroute!
Normal queue (for all flows)
Reroute “only if” there is no inflight out-of-order packets
 Enable switch to reorder a flow using a single reorder queue
Key Idea

## Slide 23: Cautious Rerouting
ConWeave SrcToR
ConWeave DstToR
T
Reroute!
Out-of-order!
Normal queue (for all flows)
Reroute “only if” there is no inflight out-of-order packets
 Enable switch to reorder a flow using a single reorder queue
Key Idea

## Slide 24: Cautious Rerouting
ConWeave SrcToR
ConWeave DstToR
T
Reroute!
Dynamically assign reorder queue!
Reorder queue
Normal queue (for all flows)
Reroute “only if” there is no inflight out-of-order packets
 Enable switch to reorder a flow using a single reorder queue
Key Idea

## Slide 25: Cautious Rerouting
ConWeave SrcToR
ConWeave DstToR
T
Reroute!
Normal queue (for all flows)
“TAIL” says that all packets from OLD path have arrived
 Flush reorder queue
Reorder queue
Reroute “only if” there is no inflight out-of-order packets
 Enable switch to reorder a flow using a single reorder queue
Key Idea

## Slide 26: Cautious Rerouting
ConWeave SrcToR
ConWeave DstToR
T
Reroute!
Reorder queue
Normal queue (for all flows)
Release the reorder queue, and redirect a flow to normal queue
Reroute “only if” there is no inflight out-of-order packets
 Enable switch to reorder a flow using a single reorder queue
Key Idea

## Slide 27: Cautious Rerouting
ConWeave SrcToR
ConWeave DstToR
Reroute!
”CLEAR” – no more inflight out-of-order packets
Reorder queue
Normal queue (for all flows)
Release the reorder queue, and redirect a flow to normal queue
Reroute “only if” there is no inflight out-of-order packets
 Enable switch to reorder a flow using a single reorder queue
Key Idea

## Slide 28: Cautious Rerouting
Reroute “only if” there is no inflight out-of-order packets
 Enable switch to reorder a flow using a single reorder queue
Key Idea
Normal queue (for all flows)
ConWeave DstToR
ConWeave SrcToR
”CLEAR” – no more inflight out-of-order packets
ConWeave reroutes a flow when congestion is detected* while delivering packets in order
TAIL
(1) Reroute
(2) Buffer
(3) Flush
CLEAR
* More details in the paper
(0) Monitoring*

## Slide 29: Evaluation
Experiment Setup
RoCEv2 with Lossless Ethernet (i.e., PFC-enabled)
2x4 Leaf-Spine topology with all 25G links (oversubscription ratio 2:1)
  Total 16 RDMA nodes (mix of NVIDIA CX-5 and CX-6)
Network load: 80%
RPC workload
Comparison: ECMP, Letflow[1] (flowlet ∆ = 100µs), DRILL[2] (per-packet)
[1] Let it flow: Resilient asymmetric load balancing with flowlet switching [NSDI’17]
[2] Resilient datacenter load balancing in the wild [SIGCOMM’17]

## Slide 30: ConWeave is effective in reducing RDMA FCTs
Average
99.9th-percentile
ECMP
Letflow
Flow Completion Time (µs)
DRILL
0
30
60
90
600
120
ECMP
Letflow
DRILL
0
500
1000
1500
2000
6000
ConWeave
16.8%
ConWeave
44.4%
Flowlet and per-packet rerouting performs worse than ECMP, if not on par
Avg and 99.9-percentile FCT reduction by 16.8% and 44.4%, respectively

## Slide 31: Buffer and Queue Usage Overhead for Reordering
Switches have 10’s of MBs of packet buffer and up to 128 physical queues
Experiment setup
8x8 Leaf-Spine (128 hosts), all 100Gbps links
Network load: 80%
Diverse workloads such as RPC, Storage, and Hadoop
Maximum size of buffer usage per switch
< 2.5 MB
Packet buffer overhead
Maximum number of queue usage per port < 10
Queue usage overhead

## Slide 32: Summary
ConWeave – Network Load Balancer for RDMA
RoCEv2 Compatible
Finer-granularity + in-order delivery
Path Monitoring
Agile and lightweight congestion detection
Path Selecting
Congestion-evasive rerouting
Cautious Rerouting
Tight incorporation with switch’s reordering capability
Pkt Reordering
Efficient queue flush via strict priority

## Slide 33
Thank you!
Credit of icons: flaticon.com
songch@comp.nus.edu.sg

## Slide 34: BACKUP SLIDE – ConWeave Packet Loss
Packet Loss
(TAIL, CLEAR)
TAIL loss
Queue will not be flushed
Calculate “expected TAIL arrival time” and flush if timeout
Leveraging in-band telemetry
CLEAR loss
Resume after sufficient inactive time
No more rerouting of the flow

## Slide 35: BACKUP SLIDE – Challenge. Path Monitoring
Goal: Timely monitor current path’s congestion
Notification delay = DATA (forward) delay + Piggyback (backward) delay
 Sol: Set high-prio.
 Inevitably high!
Piggyback!
Congested
SrcToR
DstToR
Probing current path
Piggybacking is slow to know a current path’s congestion

## Slide 36: BACKUP SLIDE – Challenge. Restoring Packet Order
Queue pause/ resume cap.
Intel Tofino2
~128 FIFO queues per Eg. port
Goal: Restoring packet back in-order
: Lack of sorting primitives and limited FIFO queues
Hard to restore “arbitrary” packet orders
4
3
2
1
Next SEQ = 1
Next SEQ = 2
Costly to store pkts to FIFO queues and flush them in relay
Recirculation increases more out-of-order packets
Recirc. & flushing
4
3
2
enqueue rate > flush rate
5
6
…
flush in relays

## Slide 37: BACKUP SLIDE – Motivating Results
Existing solutions perform worse than ECMP, if not on par.
Observation from our RoCEv2 Testbed
Flow Completion Time (µs)
X 8
X 8
Lossless RDMA (RoCE)
Network Load = 50%
RPC workload
: NVIDIA CX-5/6 25G Port
25G
Flowlet (timegap threshold)
Per-pkt

## Slide 38: BACKUP SLIDE – Evaluation on Simulation
Average, short msgs
Average, long msgs
Fat-tree topology with 256 hosts, 100Gbps, 60% Network Load